## Slide 1: Robotics Vision Processing
Using OpenCV, Python, and a Raspberry Pi

## Slide 2: Follow along with this power point!
You can download this power point (highly recommend so you don’t have to type out download links) by going to the github repository I created for this introduction to OpenCV at: github.com/jviszlai/opencvPythonTutorial
Click on PowerPoint.pptx, and then click on download to get the power point

## Slide 3: Things you need on your computer:
Any file zip software (WinRAR is free)
  WinRAR: www.rarlab.com/download.htm
Python (Use Version 2.7 for now)
NumPy (Required for OpenCV to work)
OpenCV (Use any version 3.0.0 or greater. 3.0.0 is fine)
Git (not related to OpenCV but needed to get some example code we will use)

## Slide 4: Installing Python 2.7 for Windows
Browse to www.python.org/downloads/ and download Python 2.7.12
Run the installer that was downloaded
Install for all users vs just for me (depends on if shared computer, doesn’t matter)
Hit next until you reach the Customize Python 2.7.12 page
Scroll down and make sure you edit “add python.exe to Path” to “will be installed on local hard drive” (VERY IMPORTANT)
Click next and after installation click finish

## Slide 5: Installing NumPy on Windows
Browse to www.lfd.uci.edu/~gohlke/pythonlibs/ and scroll down to NumPy
Download the first file under NumPy:
  numpy-1.11.2+mkl-cp27-cp27m-win32.whl
Using a file zip tool (WinRAR), right click the download file and click ”extract to ‘numpy-1.11.2+mkl-cp27-cp27m-win32’”
Browse into the newly created folder and copy the folder named numpy
On your computer, browse to: C:/Python27/Lib/site-packages/ and paste the numpy folder

## Slide 6: Installing OpenCV on Windows
Browse to www.opencv.org/downloads.html
Scroll down and under Version 3.0 click OpenCV for Windows
Run the opencv-3.0.0.exe file you downloaded
Click extract
Copy the newly created opencv folder into C:
On your computer, browse to: C:/opencv/build/python/2.7/x86/
  Copy the cv2.pyd file
Paste the file in the same directory we put NumPy
  The directory is: C:/Python27/Lib/site-packages/

## Slide 7: Installing Git on Windows
First, browse to: https://git-scm.com/downloads and click on Windows
Run the file you downloaded and click next until you get to Adjusting your PATH environment
Make sure to select Run Git from Windows Command Prompt
Click next until the installation begins
After installation, you can deselect to view the release notes (unless you really want to) and click finish

## Slide 8: Getting the project we’re working on
Open the command prompt and browse to an easily accessible directory (Desktop is fine) (you can do this by typing ‘cd Desktop’)
Then in the command prompt type:
  ‘git clone https://github.com/jviszlai/opencvPythonTutorial.git’
This should create a new folder called opencvPythonTutorial in your Desktop (or whatever directory you were in)
In the command prompt, browse to this folder by typing:
  ’cd opencvPythonTutorial’ (cd is the change directory command)
  Make sure to stay in this directory for the rest of the power point
In the command prompt, checkout the first version of the project with ‘git checkout v1.0’ As we progress, simply checkout the next version (for example the next version after this is v1.1, then v1.2, etc.)

## Slide 9: OpenCV: The Basics
Using your text editor, open the exampleVideo.py file located in the project folder
This is an example of simply getting video input and converting it to black and white
To run the file, in your command prompt type:
  ‘python exampleVideo.py’
  The command to run any python file is ‘python [file]”
  Note: python files will always end in .py!
This should grab video from your first available camera (generally a webcam if your computer has one) and display it in black and white
You can close the window and exit the program by pressing q

## Slide 10: OpenCV: Creating a red object detector v1.0
In your text editor, open up findRed.py
This first version only converts the video feed to an HSV color space
HSV is an alternative to RGB that instead of storing colors based on Red, Green, and Blue, stores them based on Hue, Saturation, and Value (Brightness)
This is much better for vision processing, if you want more information on why, the wiki page has a good description: https://en.wikipedia.org/wiki/HSL_and_HSV#Use_in_image_analysis
Note: In OpenCV the HSV value ranges are: H: 0-180, S: 0-255, V: 0-255
  This is different from what many photo editing programs may use!

## Slide 11: OpenCV: Creating a red object detector v1.1
Use git to checkout the next version of this project (v1.1)
Depending on your text editor, the findRed.py file you have open may update automatically. If not, close out of the old version (Do not save!) and reopen the file to get the new version
This version creates a range of values that we define to be red and processes the frame to display, in white, only the parts that are inside the range
Note: This range may change if the room you’re in changes (i.e. competition lighting is much different than school lighting). Be prepared to calibrate your range!
Question: Why do you think we had to make two different ranges to distinguish what is red? (Hint: look at an image for the range of colors in HSV)

## Slide 12: OpenCV: Creating a red object detector v1.2
Use git to checkout the next version of the project (v1.2)
This version uses erode and dilate to minimize the amount of small pixels that throw our accuracy in finding the object we want
Note: this is definitely not a crucial step, it only slightly improves the video processing

## Slide 13: OpenCV: Creating a red object detector v1.3
Use git to checkout the next version of the project (v1.3)
This version uses findContours to get all the areas of red from our previous filter that kept only what matched our range of red
It also displays all these areas using drawContours
Question: Notice there are multiple false detections along with the object we want. What would be a way to differentiate our desired object from the others? (There are many different approaches!)

## Slide 14: OpenCV: Creating a red object detector v1.4
Use git to checkout the next version of the project (v1.4)
This version uses a very simple approach to find the object we want: it calculates the size, using contourArea, of all the different detected areas, and only keeps the largest one
Note: Using a For loop (a loop that is present in virtually every programming language) we can easily traverse through all the areas we previously detected!
After determining the largest area, we can remove the other areas and only keep the largest (which should be the object we want)

## Slide 15: OpenCV: Creating a red object detector v1.5
Use git to checkout the next version of the project (v1.5)
This version finalizes the filtering we did by combining the final version of the mask (which had singled out the largest area (which should be the red object we wanted)) with the original frame, using bitwise_and
If we display the original frame next to this finalized frame, we can see that our program has successfully identified the red object of interest!

## Slide 16: Other projects you can see!
One of the great things about GitHub is that it has thousands of projects other people have created that you can see!
The GitHub for OpenCV, for example: https://github.com/opencv/opencv, has multiple sample programs you can look for, just go to samples and then python
One of these programs I slightly modified to process video input, and included in this project. It’s called findSquares.py and should outline any squares it can see in the video input